## Slide 1
RCVC
Red Circle
Valve Controller
How It Works
ver 022421

## Slide 2: RCVC How It Works – STEADY STATE – 50% TRAVEL – NO EMISSIONS
CLOSE = OFF
OPEN = OFF
Adjust Orifices
(Optional)
Supply Regulator
Line Pressure
24 VDC Power
RHPA-DA Actuator
VALVE POSITION = 50%
STATIC
PRCV Pipeline Rotary Control Valve
Feedback Signal = 12 mA
Command Signal = 12 mA
EX = NONE
COM 50%
POS 50%

## Slide 3: RCVC How It Works – OPEN SIGNAL APPLIED – MOVING - EMISSIONS
CLOSE = OFF
OPEN = ON
Adjust Orifices
(Optional)
Supply Regulator
Line Pressure
24 VDC Power
RHPA-DA Actuator
VALVE POSITION >50%
MOVING OPEN
PRCV Pipeline Rotary Control Valve
Feedback Signal = >12 mA
Command Signal = 16 mA
EX = YES
COM 75%
POS 62%

## Slide 4: RCVC How It Works – STEADY STATE – 75% TRAVEL – NO EMISSIONS
CLOSE = OFF
OPEN = OFF
Adjust Orifices
(Optional)
Supply Regulator
Line Pressure
24 VDC Power
RHPA-DA Actuator
VALVE POSITION = 75%
STATIC
PRCV Pipeline Rotary Control Valve
Feedback Signal = 16 mA
Command Signal = 16 mA
EX = NONE
COM 75%
POS 75%

## Slide 5: RCVC How It Works – CLOSE SIGNAL APPLIED – MOVING - EMISSIONS
CLOSE = ON
OPEN = OFF
Adjust Orifices
(Optional)
Supply Regulator
Line Pressure
24 VDC Power
RHPA-DA Actuator
VALVE POSITION <75%
MOVING CLOSED
PRCV Pipeline Rotary Control Valve
Feedback Signal = <16 mA
Command Signal = 8 mA
EX = YES
COM 75%
POS 62%

## Slide 6: RCVC How It Works – STEADY STATE – 25% TRAVEL – NO EMISSIONS
CLOSE = OFF
OPEN = OFF
Adjust Orifices
(Optional)
Supply Regulator
Line Pressure
24 VDC Power
RHPA-DA Actuator
VALVE POSITION = 25%
STATIC
PRCV Pipeline Rotary Control Valve
Feedback Signal = 8 mA
Command Signal = 8 mA
EX = NONE
COM 25%
POS 25%

## Slide 7: RCVC How it Works – STEADY STATE – 50% TRAVEL – NO EMISSIONS
CLOSE
Signal
OPEN
Signal
Supply Regulator
Line Pressure
RHPA-SR
Actuator
PRCV Pipeline Rotary Control Valve
Feedback Signal = 12 mA
EX
S
S
Spring to
CLOSE
24 VDC Power
Command Signal = 12 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
Class 1, Div 1
VALVE POSITION = 50%
STATIC
COM 50%
POS 50%

## Slide 8: RCVC How it Works – OPEN SIGNAL APPLIED – MOVING – NO EMISSIONS
CLOSE
Signal
OPEN
Signal
Supply Regulator
Line Pressure
RHPA-SR
Actuator
PRCV Pipeline Rotary Control Valve
Feedback Signal = >12 mA
EX
S
S
Spring to
CLOSE
24 VDC Power
Command Signal = 16 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
Class 1, Div 1
VALVE POSITION >50%
MOVING OPEN
COM 75%
POS 50%

## Slide 9: RCVC How it Works– STEADY STATE – 75% TRAVEL – NO EMISSIONS
CLOSE
Signal
OPEN
Signal
Supply Regulator
Line Pressure
RHPA-SR
Actuator
PRCV Pipeline Rotary Control Valve
Feedback Signal = 16 mA
EX
S
S
Spring to
CLOSE
24 VDC Power
Command Signal = 16 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
Class 1, Div 1
VALVE POSITION = 75%
STATIC
COM 75%
POS 75%

## Slide 10: RCVC How it Works – CLOSE SIGNAL APPLIED – MOVING - EMISSIONS
CLOSE
Signal
OPEN
Signal
Supply Regulator
Line Pressure
RHPA-SR
Actuator
PRCV Pipeline Rotary Control Valve
Feedback Signal = >12 mA
EX
S
S
Spring to
CLOSE
24 VDC Power
Command Signal = 16 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
Class 1, Div 1
VALVE POSITION <75%
MOVING CLOSED
COM 75%
POS 50%

## Slide 11: RCVC How it Works – STEADY STATE – 25% TRAVEL – NO EMISSIONS
CLOSE
Signal
OPEN
Signal
Supply Regulator
Line Pressure
RHPA-SR
Actuator
PRCV Pipeline Rotary Control Valve
Feedback Signal = 8 mA
EX
S
S
Spring to
CLOSE
24 VDC Power
Command Signal = 8 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
Class 1, Div 1
VALVE POSITION 25%
STATIC
COM 25%
POS 25%

## Slide 12: RCVC How it Works – STEADY STATE – 50% TRAVEL – NO EMISSIONS
OPEN
Signal
CLOSE
Signal
Supply Regulator
Line Pressure
LD Series Linear Diaphragm Actuator
CVET Series
Control Valve
Feedback Signal = 12 mA
EX
S
S
Spring to
OPEN
24 VDC Power
Command Signal = 12 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
COM 50%
POS 50%
VALVE POSITION 50%
STATIC

## Slide 13: RCVC How it Works – OPEN SIGNAL APPLIED – MOVING – EMISSIONS
OPEN
Signal
CLOSE
Signal
Supply Regulator
Line Pressure
LD Series Linear Diaphragm Actuator
CVET Series
Control Valve
Feedback Signal >12 mA
EX
S
S
Spring to
OPEN
24 VDC Power
Command Signal = 16 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
COM 75%
POS 50%
VALVE POSITION >50%
MOVING OPEN

## Slide 14: RCVC How it Works – STEADY STATE – 75% TRAVEL – NO EMISSIONS
OPEN
Signal
CLOSE
Signal
Supply Regulator
Line Pressure
LD Series Linear Diaphragm Actuator
CVET Series
Control Valve
Feedback Signal = 16 mA
EX
S
S
Spring to
OPEN
24 VDC Power
Command Signal = 16 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
COM 75%
POS 75%
VALVE POSITION 75%
STATIC

## Slide 15: RCVC How it Works – CLOSE SIGNAL APPLIED – MOVING – NO EMISSIONS
OPEN
Signal
CLOSE
Signal
Supply Regulator
Line Pressure
LD Series Linear Diaphragm Actuator
CVET Series
Control Valve
Feedback Signal <16 mA
EX
S
S
Spring to
OPEN
24 VDC Power
Command Signal = 8 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
COM 25%
POS 75%
VALVE POSITION <75%
MOVING CLOSED

## Slide 16: RCVC How it Works – STEADY STATE – 25% TRAVEL – NO EMISSIONS
OPEN
Signal
CLOSE
Signal
Supply Regulator
Line Pressure
LD Series Linear Diaphragm Actuator
CVET Series
Control Valve
Feedback Signal = 8 mA
EX
S
S
Spring to
OPEN
24 VDC Power
Command Signal = 8 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
COM 25%
POS 25%
VALVE POSITION 25%
STATIC

## Slide 17: RCVC w PCO How it Works – RCVC in Control – PCO Disengaged
OPEN
Signal
CLOSE
Signal
Supply Regulator
Line Pressure
LD Series Linear Diaphragm Actuator
CVET Series
Control Valve
Feedback Signal = 12 mA
EX
S
S
Spring to
OPEN
24 VDC Power
Command Signal = 12 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
P2
HSR
Downstream
Pressure
VPC-SA-BV
Setpoint 750 psig
P2 = 650 psig
SUPPLY
OUTPUT
SENSING
EX
VALVE POSITION 50%
STATIC
IN 1
IN 2
OUT
OUTRCVC > OUTVPC
COM 50%
POS 50%

## Slide 18: RCVC w PCO How it Works – VPC-SA-BV in Control – PCO Engaged
OPEN
Signal
CLOSE
Signal
Supply Regulator
Line Pressure
LD Series Linear Diaphragm Actuator
CVET Series
Control Valve
Feedback Signal = 12 mA
EX
S
S
Spring to
OPEN
24 VDC Power
Command Signal = 12 mA
HART Handheld Communicator
RED CIRCLE
VALVE CONTROLLER
P2
HSR
Downstream
Pressure
VPC-SA-BV
Setpoint 750 psig
P2 = 750 psig
SUPPLY
OUTPUT
SENSING
EX
VALVE POSITION <50%
MODULATING
VPC IN CONTROL AT 750 PSIG
IN 1
IN 2
OUT
OUTRCVC < OUTVPC
COM 50%
POS 50%

## Slide 19: Our Contact Information
VRG Controls, LLC
Toll-Free: +844-FLOW-VRG (USA & CANADA)
e-Mail: Sales@VRGControls.com
www.VRGControls.com
VRG Controls, LLC
1199 Flex Court, Unit B
Lake Zurich, Illinois 60047 USA
VRG Controls, LLC
Solutions for Natural Gas!
Follow Us: