## Slide 1
VRG Controls
Emissions Reduction
Solutions
05/24/22

## Slide 2: High Capacity Control Valves For Natural Gas Pipelines
PRCV Pipeline Rotary Control Valve
Typ. Double Acting Configuration

## Slide 3: VPC Series Valve Regulator Pilots
Pneumatic Pressure Control Instrumentation for Use with Natural Gas Control Valves
Can Replace Venting Pressure Controllers to Reduce Emissions
Can Replace Becker VRP Pilots for Improved Performance and Reliability
Major Technological Advancements as Compared to Our Competition

## Slide 4: Next Generation of Valve Pilot Controllers
SIX (6) Common Control Springs Across All Models
All STAINLESS STEEL Internal Components
Larger Diameter Diaphragms Provide Greater Sensitivity (20% Increase in Area vs. Competition)
High Strength Setpoint Screw Design Includes Protective Cover
Patented* Manifold Design Provides Modular Format and Improved Dynamic Performance
Setpoints Available From 3.0 psig to 1500 psig
Environmentally Friendly Design Can Exhibit ZERO Steady State Emissions
Bleed to Pressure System Features Eliminates all Atmospheric Emissions

## Slide 5: Compatible To Retrofit / Replace Existing Pneumatic Pressure Controllers

## Slide 6: VPC’s Better Than EPA Emissions Performance Mandate

## Slide 7: VPC Valve Pilot Controllers – 5 Plug & Play Configurations
Logic XChange

## Slide 8: VPC Schematic #1 – VPC-DA-BV + NVD + ATM Ex – RHPA-DA

## Slide 9: VPC Schematic #2 – VPC-DA-SN + NVD + Discharge Pressure + RHPA-DA

## Slide 10: VPC Schematic #3 – VPC-SA-BV + ATM Ex + LD Actuator

## Slide 11: VPC Schematic #4 – VPC-SA-BV + ATM Ex + LD Actuator + Remote Set

## Slide 12: VPC Schematic #5 – VPC-SA-BV + ATM Ex – RHPA-SR

## Slide 13: VPC Schematic #6 – VPC-SA-BV + ATM Ex – RHPA-SR

## Slide 14: RCVC Red Circle Valve Controller
Hi Resolution Color TFT Programmable Display with Intuitive and Easy Read Menu
Class 1, Div. 1 Ex Proof Terminal Strip Housing Provides Generous Room for Easy Wire Termination
Rotary Control Switch Provides Non-Invasive Menu Navigation and Setup
RCVC Electrical Ports and Mounting Brackets Provide Flexible Configuration. 100% Compatible with Existing Becker/GE DNGP & EFP Enclosures for Easy Retrofit
HART Protocol Communication Standard. Wireless Bluetooth Capable for Easy Configuration and Evaluation. Bluetooth May Be Disabled as Desired.
4-20 mA Analog Command Signal Input OR ±24 VDC Discrete Pulse Positioning
ZERO Steady State Emissions with Ability to Discharge to Pressure System for Complete Atmospheric Emissions.
RCVC May be Installed Directly on Control Valve or Remotely in Control Cabinet or RTU Building
RED
CIRCLE
VALVE CONTROLER
PLUG & PLAY REPLACEMENT FOR BECKER/GE DNGP POSITIONER

## Slide 15: RCVC Red Circle Valve Controller – Typical RHPA-DA Schematic
CLOSE
Signal
OPEN
Signal
RED CIRCLE
VALVE CONTROLLER
Class 1, Div 1
Adjust Orifices
(Optional)
Supply Regulator
Line Pressure
24 VDC Power
RHPA-DA
Rotary High Pressure Actuator
Micropulse Linear Position Sensor
PRCV Pipeline Rotary Control Valve
4-20 mA Feedback Signal
4-20 mA Command Signal
EX
HART Handheld Communicator
RED
CIRCLE
VALVE CONTROLER

## Slide 16: Interchangeable Linear Power Modules Crank Arm Actuators - AG
ELECTRO-HYDRAULIC ACTUATOR POWER MODULE (LINEAR OUTPUT) | ELECTRIC ACTUATOR POWER MODULE (LINEAR OUTPUT) | PNEUMATIC ACTUATOR POWER MODULE (LINEAR OUTPUT)
VRG Controls RHPA Actuator
OR
Becker RPDA/RPSR Actuator
This Photo by Unknown Author is licensed under CC BY
Above Ground Installation

## Slide 17: Skilmatic SI (Linear) Range – Electro Hydraulic Actuators
Notes:
1-Phase AC OR 24 VDC Power Required to Obtain Modulating Duty Infinite STARTS/HR
Direct Replace VRG RHPA Linear Piston
Can Retrofit to Existing VRG Below Ground Control Valves
Standard adaptations for VRG or Becker Existing Installations
Has Failsafe Options

## Slide 18: Skilmatic SI (Rotary) Range – Electro Hydraulic Actuators
Notes:
1-Phase AC OR 24 VDC Power Required to Obtain Modulating Duty Infinite STARTS/HR
Direct Drive w Control Valve Stem
Pair w Rotork Quarter Turn Gear Assembly
Can Retrofit to Exist Quarter Turn Control Valves
Cannot Retrofit to Existing VRG Below Ground Control Valves (Need Linear)
Has Failsafe Options

## Slide 19: Rotork IQM – Quarter Turn Modulating Service
Notes:
3-Phase AC Power Required to Obtain Modulating Duty > 1200 STARTS / HR
Direct Drive w Control Valve Stem
Pair w Rotork Quarter Turn Gear Assembly
Can Retrofit to Exist Quarter Turn Control Valves
Cannot Retrofit to Existing VRG Below Ground Control Valves (Need Linear)
Has Failsafe Options

## Slide 20: Rotork IQM – Quarter Turn Modulating Service

## Slide 21: IQML – Linear Modulating
Notes:
3-Phase AC Power Required to Obtain Modulating Duty > 1200 STARTS / HR
Direct Replace VRG RHPA Linear Piston
Can Retrofit to Existing VRG Below Ground Control Valves
Standard adaptations for VRG or Becker Existing Installations
Has Failsafe Options

## Slide 22: Below Ground Option - Key Design Considerations
PRCV Seat Seals Extended Above Ground
All Port Extension Lines ASME Code Welded and Hydro-tested
Stem Lubrication / Test Extended
Drain Line / Blowdown Extended
Tail-rod Instrument Mounting System Standard
Vented Actuator Housing
Coal Tar Epoxy Coating on Below Ground Portion
Fully Welded Bracket Supports on All Lines

## Slide 23: Interchangeable Linear Power Modules Crank Arm Actuators - BG
VRG Controls RHPA Actuator
OR
Becker RPDA/RPSR Actuator
ELECTRO-HYDRAULIC ACTUATOR POWER MODULE (LINEAR OUTPUT) | ELECTRIC ACTUATOR POWER MODULE (LINEAR OUTPUT) | PNEUMATIC ACTUATOR POWER MODULE (LINEAR OUTPUT)
Below Ground Installation

## Slide 24: Example – Below Ground Pneumatic Monitor Control Valve

## Slide 25: Example – Below Ground Electric Actuator Worker Control Valve
NON STANDARD DESIGN W
VERTICAL STEM EXTENSION

## Slide 26: Variety of Controls / Actuation Options to Reduce Emissions
 | RHPA Actuator | RHPA Actuator | RHPA Actuator | IS Series | IQM Series
Power | Pneumatic | Pneumatic | Pneumatic | VDC 1-Phase AC | 3-Phase AC
Concept | Ex ATM | Discharge to Pressure | Capture by Combustion | Electro Hydraulic | Electric
Available Failsafe | Lock Last Fail Open Fail Closed | Lock Last Fail Open Fail Closed | Lock Last Fail Open Fail Closed | Lock Last Fail Open Fail Closed | Lock Last
Quarter Turn | YES | YES | YES | YES | YES
Interchangeable Linear | YES | YES | YES | YES | YES
End of Travel Emissions | ZERO | ZERO | ZERO | ZERO | ZERO
Steady State Control Emissions | ZERO | ZERO | ZERO | ZERO | ZERO
Transient Emissions | YES | ZERO | ZERO | ZERO | ZERO

## Slide 27
FLOW
P1
P2
MONITOR
CONTROL
VALVE
(STANDBY)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
WORKER
CONTROL
VALVE
(ACTIVE)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
 | MONITOR | WORKER
CONTROL | VPC SERIES | VPC SERIES
ACTUATOR | RHPA SERIES | RHPA SERIES
ENERGY | PNEUMATIC | PNEUMATIC
SIGNAL | PNEUMATIC | PNEUMATIC
STEADY EMISSIONS | ZERO | ZERO
TRANSIENT EMISSIONS | **ACTUATOR DISPLACE | **ACTUATOR DISCPLACE
CONFIGURATION: 1 - ALL PNEUMATIC PRESSURE CONTROL ATM DISCH
EX
EX
**REFERENCE VRG CONTROL TRANSIENT EMISSONS CALCULATOR FOR DETAILS
NOTES:
PRESSURE CONTROL APPLICATIONS ONLY
ALL PNEUMATIC – NO ELECTRICAL POWER REQUIRED
SELF-CONTAINED AND RELIABLE
LOW COST
ELIMINATES MOST ATMOSPHERIC EMISSIONS
Date | 03/23/22 | Title | EMISSIONS REDUX – CONFIGURAITON 1
Rev. | 0 | Customer | VRG CONTROLS
Configuration 1 – Emissions Reduction

## Slide 28
FLOW
P1
P2
MONITOR
CONTROL
VALVE
(STANDBY)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
WORKER
CONTROL
VALVE
(ACTIVE)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
EX
 | MONITOR | WORKER
CONTROL | VPC SERIES | VPC SERIES
ACTUATOR | RHPA SERIES | RHPA SERIES
ENERGY | PNEUMATIC | PNEUMATIC
SIGNAL | PNEUMATIC | PNEUMATIC
STEADY EMISSIONS | ZERO | CAPTURED
TRANSIENT EMISSIONS | **ACT DISPLACE | CAPTURED
CONFIGURATION: 2 - ALL PNEUMATIC PRESSURE CONTROL CAPTURED EMISSIONS
EX
**REFERENCE VRG CONTROL TRANSIENT EMISSONS CALCULATOR FOR DETAILS
NOTES:
PRESSURE CONTROL APPLICATIONS ONLY
ALL PNEUMATIC – NO ELECTRICAL POWER REQUIRED
SELF-CONTAINED AND RELIABLE
LOW COST
ZERO ATMOSPHERIC EMISSIONS – WORKER
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
REQURIES SUITABLE DP BETWEEN SUPPLY & DISCHARGE
Date | 03/23/22 | Title | EMISSIONS REDUX – CONFIGURAITON 2
Rev. | 0 | Customer | VRG CONTROLS
Configuration 2 – Emissions Reduction

## Slide 29
FLOW
P1
P2
MONITOR
CONTROL
VALVE
(STANDBY)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
WORKER
CONTROL
VALVE
(ACTIVE)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
EX
 | MONITOR | WORKER
CONTROL | VPC SERIES | VPC SERIES
ACTUATOR | RHPA SERIES | RHPA SERIES
ENERGY | PNEUMATIC | PNEUMATIC
SIGNAL | PNEUMATIC | PNEUMATIC
STEADY EMISSIONS | ZERO | CAPTURED
TRANSIENT EMISSIONS | **ACT DISPLACE | CAPTURED
CONFIGURATION: 3 - ALL PNEUMATIC PRESSURE CONTROL CAPTURED BY COMBUSTION EMISSIONS
EX
**REFERENCE VRG CONTROL TRANSIENT EMISSONS CALCULATOR FOR DETAILS
DEDICATED CATALYTIC
HEATER OR PIPELINE HEATER
NOTES:
PRESSURE CONTROL APPLICATIONS ONLY
ALL PNEUMATIC – NO ELECTRICAL POWER REQUIRED
SELF-CONTAINED AND RELIABLE
LOW COST
ZERO ATMOSPHERIC EMISSIONS – WORKER
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
REQURIES SUITABLE DP BETWEEN SUPPLY & DISCHARGE
CAN DISCHARGE TO NEARBY PIPELINE HEATER OR DEDICATED CATALYTIC
Date | 03/23/22 | Title | EMISSIONS REDUX – CONFIGURAITON 3
Rev. | 0 | Customer | VRG CONTROLS
Configuration 3 – Emissions Reduction

## Slide 30
FLOW
P1
P2
MONITOR
CONTROL
VALVE
(STANDBY)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
XT
WORKER
CONTROL
VALVE
(ACTIVE)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
RCVC
RED CIRCLE
VALVE
CONTROLLER
 | MONITOR | WORKER
CONTROL | VPC SERIES | RCVC SERIES
ACTUATOR | RHPA SERIES | RHPA SERIES
ENERGY | PNEUMATIC | PNEUMATIC
SIGNAL | PNEUMATIC | 4-20 MA ELECTRIC
STEADY EMISSIONS | ZERO | ZERO
TRANSIENT EMISSIONS | ACT DISPLACE | ACT DISCPLACE
CONFIGURATION: 4 – ELECTRO-PNEUM WORKER W PNEUMATIC MONITOR – ATM DISCHARGE
EX
4-20 MA COMMAND SIGNAL
4-20 MA FEEDBACK SIGNAL
EX
NOTES:
VOLUMETRIC OR PRESSURE CONTROL APPLICATIONS
ELECTRO PNEUMAITC WORKER REQUIRES POWER AND LOGIC
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
Date | 03/23/22 | Title | EMISSIONS REDUX – CONFIGURAITON 4
Rev. | 0 | Customer | VRG CONTROLS
Configuration 4 – Emissions Reduction

## Slide 31
FLOW
P1
P2
MONITOR
CONTROL
VALVE
(STANDBY)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
XT
WORKER
CONTROL
VALVE
(ACTIVE)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
RCVC
RED CIRCLE
VALVE
CONTROLLER
 | MONITOR | WORKER
CONTROL | VPC SERIES | RCVC SERIES
ACTUATOR | RHPA SERIES | RHPA SERIES
ENERGY | PNEUMATIC | PNEUMATIC
SIGNAL | PNEUMATIC | 4-20 MA ELECTRIC
STEADY EMISSIONS | ZERO | CAPTURED
TRANSIENT EMISSIONS | ACT DISPLACE | CAPTURED
CONFIGURATION: 5 – ELECTRO-PNEUM WORKER W PNEUMATIC MONITOR – CAPTURED EMISSIONS
4-20 MA COMMAND SIGNAL
4-20 MA FEEDBACK SIGNAL
EX
EX
NOTES:
VOLUMETRIC OR PRESSURE CONTROL APPLICATIONS
ELECTRO PNEUMAITC WORKER REQUIRES POWER AND LOGIC
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
ZERO ATMOSPHERIC EMISSIONS – WORKER
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
REQURIES SUITABLE DP BETWEEN SUPPLY & DISCHARGE
Date | 03/23/22 | Title | EMISSIONS REDUX – CONFIGURAITON 5
Rev. | 0 | Customer | VRG CONTROLS
Configuration 5 – Emissions Reduction

## Slide 32
FLOW
P1
P2
MONITOR
CONTROL
VALVE
(STANDBY)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
XT
WORKER
CONTROL
VALVE
(ACTIVE)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
RCVC
RED CIRCLE
VALVE
CONTROLLER
 | MONITOR | WORKER
CONTROL | VPC SERIES | RCVC SERIES
ACTUATOR | RHPA SERIES | RHPA SERIES
ENERGY | PNEUMATIC | PNEUMATIC
SIGNAL | PNEUMATIC | 4-20 MA ELECTRIC
STEADY EMISSIONS | ZERO | CAPTURED COMBUSTION
TRANSIENT EMISSIONS | ACT DISPLACE | CAPTURED COMBUSTION
CONFIGURATION: 6 – ELECTRO-PNEUM WORKER W PNEUMATIC MONITOR – CAPTURED BY COMBUSTION EMISSIONS
4-20 MA COMMAND SIGNAL
4-20 MA FEEDBACK SIGNAL
DEDICATED CATALYTIC
HEATER OR PIPELINE HEATER
EX
EX
NOTES:
VOLUMETRIC OR PRESSURE CONTROL APPLICATIONS
ELECTRO PNEUMAITC WORKER REQUIRES POWER AND LOGIC
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
ZERO ATMOSPHERIC EMISSIONS – WORKER
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
REQURIES SUITABLE DP BETWEEN SUPPLY & DISCHARGE
CAN DISCHARGE TO NEARBY PIPELINE HEATER OR DEDICATED CATALYTIC
Date | 03/23/22 | Title | EMISSIONS REDUX – CONFIGURAITON 6
Rev. | 0 | Customer | VRG CONTROLS
Configuration 6 – Emissions Reduction

## Slide 33
Date | 03/23/22 | Title | EMISSIONS REDUX – CONFIGURAITON 7
Rev. | 0 | Customer | VRG CONTROLS
FLOW
P1
P2
MONITOR
CONTROL
VALVE
(STANDBY)
SGS
SUPPLY
GAS
SYSTEM
VMO-150
VALVE
MANUAL
OVERRIDE
VPC
VALVE
PILOT
CONTROLLER
M
WORKER
CONTROL
VALVE
(ACTIVE)
SGS
SUPPLY
GAS
SYSTEM
ELECTRIC OR
ELECTRO-HYDRAULIC
ACTUATOR
 | MONITOR | WORKER
CONTROL | VPC SERIES | RCVC SERIES
ACTUATOR | RHPA SERIES | RHPA SERIES
ENERGY | PNEUMATIC | PNEUMATIC
SIGNAL | PNEUMATIC | 4-20 MA ELECTRIC
STEADY EMISSIONS | ZERO | CAPTURED COMBUSTION
TRANSIENT EMISSIONS | ACT DISPLACE | CAPTURED COMBUSTION
CONFIGURATION: 7 – ELECTRO-PNEUM WORKER W PNEUMATIC MONITOR – CAPTURED BY COMBUSTION EMISSIONS
4-20 MA COMMAND SIGNAL
4-20 MA FEEDBACK SIGNAL
ELECTRICAL POWER OPTIONS:
3-PHASE AC
1-PHASE AC
24 VDC
EX
NOTES:
VOLUMETRIC OR PRESSURE CONTROL APPLICATIONS
ELECTRIC WORKER REQUIRES POWER AND LOGIC
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
ZERO ATMOSPHERIC EMISSIONS – WORKER
MONITOR ONLY EMISSIONS IF “AOC” OPP OCCURENCE
PNEUMATIC MONITOR GUARANTEED OPP PROTECTION
Configuration 7 – Emissions Reduction

## Slide 34
Carbon Capture by Combustion Solution

## Slide 35
Oxford Flow
Control
Regulator
Technologies
03/23/22

## Slide 36: Title Here

## Slide 37: IM Series Wafer Style Regulators

## Slide 38: IM Series Wafer Style Regulators

## Slide 39: IHF Series Cartridge Style Regulators

## Slide 40: IHF Series Cartridge Style Regulators

## Slide 41: ES Axial Control Valve

## Slide 42: ES Axial Control Valve
RED
CIRCLE
VALVE CONTROLER

## Slide 43: 14 IN Axial Type Liquid Surge Reliever

## Slide 44: Our Contact Information
VRG Controls, LLC
Toll-Free: +844-FLOW-VRG (USA & CANADA)
e-Mail: Sales@VRGControls.com
www.VRGControls.com
VRG Controls, LLC
1199 Flex Court, Unit B
Lake Zurich, Illinois 60047 USA
VRG Controls, LLC
Solutions for Natural Gas!
Follow Us: